## Slide 1: MIPS Arithmetic
All instructions have 3 operands
  One destination, two operands
Operand order is fixed (destination first)
  Example: C code: a = b + c MIPS code: add a,b,c
  C code: a = b + c + d; MIPS code: add a, b, c add a, a, d
  Design principle: Hardware implementation is simplified via regularity
Operands must be registers in MIPS
  Register set of a machine is a limited number of special locations built directly into the hardware
Notes:   Keep Hardware simple via regularity

## Slide 2: Assembly Variables: Registers
Unlike HLL, assembly cannot use variables
  Why not? Keep hardware simple
Different operand locations for different architectures
  Stack, register, memory or a mix of them
  Every architecture design after 1980 uses a load-store register architecture: ALU operands are all registers; memory can only be accessed with load/store
Advantages of load-store register architectures
  Registers are faster than memory
  Registers are more efficient for a compiler to use
Drawback: the no. of registers is predetermined
  Assembly code must be very carefully put together to efficiently use registers
Notes:   Register-register: MIPS, SPARC, PowerPC, DEC Alpha
  Registers are directly in hardware, they are very fast (less than 1 billionth of a second)
  More efficient than other forms of internal storage

## Slide 3: MIPS Registers
32 registers in MIPS
  Why 32? Design principle: Smaller is faster
  Registers are numbered from 0 to 31
Each register can be referred to by number or name
  Number references: $0, $1, … $30, $31
  By convention, each register also has a name to make it easier to code
    $t0 - $t7 for temporary variables ($8- $15)
    $ra for return address
Each MIPS register is 32 bits wide
  Groups of 32 bits called a word in MIPS

## Slide 4: MIPS Arithmetic with Registers
MIPS Example
  C code: a = b + c MIPS code: add $s1,$s2,$s3
  C code: a = b + c + d; MIPS code: add $t1,$s2,$s3 add $s1,$t1,$s4
  $s0-$s7 conventionally are used for registers that correspond to variables in C/Java programs ($16-$23)

## Slide 5: MIPS Instructions
Syntax of instructions:
  op dest, src1, src2
  Op: operation by name
  Dest: operand getting result (“destination”)
  Src1: 1st operand for operation (“source1”)
  Src2: 2nd operand for operation (“source2”)
Each line of assembly code contains at most 1 instruction
Hash (#) is used for MIPS comments
  Anything from hash mark to end of line is a comment and will be ignored
  Every line of your comments must start with a #

## Slide 6: Addition/Subtraction Example
How to do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add $t0, $s1, $s2 #temp = b + c
  add $t0, $t0, $s3 #temp = temp + d
  sub $s0, $t0, $s4 #a = temp - e
Notice
  A single line of C code may break up into several lines of MIPS code
  May need to use temporary registers ($t0 - $t9) for intermediate results
  Everything after the hash mark on each line is ignored (comments)

## Slide 7: Constant or Immediate Operands
Immediates are numerical constants
  They appear often in code, so there are special instructions for them
  Design principle: Make the common case fast
Add Immediate:
  C code : f = g + 10
  MIPS code: addi $s0,$s1,10
    MIPS registers $s0, $s1 are associated with C variables f, g
  Syntax similar to add instruction, except that last argument is a number instead of a register
  How about subtraction? subi?

## Slide 8: Constant or Immediate Operands
There is NO subtract immediate instruction in MIPS: Why?
  ISA design principle: limit types of operations that can be done to minimum
  If an operation can be decomposed into a simpler operation, do not include it
  addi …, -X = subi …, X => so no subi
Example
  C code: f = g - 10
  MIPS code: addi $s0,$s1,-10
    MIPS registers $s0,$s1 are associated with C variables f, g

## Slide 9: Register Zero
One particular immediate, the number zero (0), appears very often in code
So we define register zero ($0 or $zero) to always have the value 0
  Often used to move values or set constant values
  f = g (in C)
  add $s0,$s1,$zero (in MIPS)
    MIPS registers $s0, $s1 are associated with C variables f, g
$zero defined in hardware
  Instruction add $zero,$zero,$s0 will not do anything!

## Slide 10: Memory Organization
Viewed as a large, single-dimension array
A memory address is an index into the array
  "Byte addressing" means that the index points to a byte of memory
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 11: Memory Organization
Bytes are nice, but most data items use larger "words"
  For MIPS, a word is 32 bits or 4 bytes
MIPS register holds 32 bits of data
  232 bytes with byte addresses from 0 to 232-1
  230 words with byte addresses 0, 4, 8, ... 232-4
Words are aligned: they must start at addresses that are multiples of 4
0
4
8
12
...
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Notes: i.e., what are the least 2 significant bits of a word address?

## Slide 12: Specify Memory Addresses
To transfer data, we need to specify:
  Register: specify this by number ($0 - $31) or symbolic name ($s0,…, $t0, …)
  Memory address: supply a pointer/index to the byte-addressed one-dimensional array
    Often, we want to be able to offset from a pointer: e.g. element A[2], date.month
The general format for a memory address offset(base register) specifying
  A register containing a pointer to memory
  A numerical offset (in bytes)
The desired memory address is the sum of these two values
  Example: 8($t0) specifies memory[$t0+8] (byte)
Notes: the memory address pointed to by the value in $t0, plus 8 bytes

## Slide 13: Data Transfer Instructions
MIPS has two basic data transfer instructions for accessing memory
lw $t0,4($s3) #load word from memory
sw $t0,8($s3) #store word to memory
Load instruction syntax: lw reg1, offset(reg2)
  Operator name: lw (meaning Load Word, so 32 bits or one word are loaded at a time)
  Reg1: register that will receive the transferred data
  Offset: a numerical offset in bytes
  Reg2: register containing pointer to memory, called base register

## Slide 14: Load Word Example
Data flow
Example: lw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then load the value from the memory pointed to by this calculated sum into register $t0
    $s0 is called the base register
    12 is called the offset
  Offset is generally used in accessing elements of array or structure: base register points to beginning of array or structure

## Slide 15: Store Instruction
Data flow
Also want to store from register into memory
  sw: meaning Store Word, so 32 bits or one word are loaded at a time)
  Store instruction syntax is identical to Load’s
Example: sw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then store the value from register $t0 into that memory address
  Remember: “Store INTO memory”

## Slide 16: Example
C code: A[12] = h + A[8]; MIPS code:
lw $t0, 32($s3) # base addr of array A in $s3
# 1 array element is 4-byte
add $t0, $s2, $t0 # h is associated with $s2 sw $t0, 48($s3) # offset=12*4=48
Can refer to registers by name (e.g., $s2, $t2) instead of number
Store word has destination last
Remember arithmetic operands are registers, not memory!
  Can’t write: add 48($s3), $s2, 32($s3)

## Slide 17: Pointers vs. Values
Key concept: a register can hold any 32-bit value
  That value can be a signed int, an unsigned int, a pointer (memory address), and so on
  If you write add $t2,$t1,$t0, then $t0 and $t1 better contain values
  If you write lw $t2,0($t0), then $t0 better contains a pointer
Don’t mix these up!

## Slide 18: Loading & Storing Bytes
In addition to word data transfers, MIPS has byte data transfers for characters (char type)
  Load byte: lb; store byte: sb
  Same format as lw, sw
What to do with other 24 bits in the 32 bit register?
  lb: sign extends to fill upper 24 bits
Normally do not want to sign extend chars
  MIPS instruction that does not sign extend when loading bytes -- load byte unsigned: lbu
…is copied to “sign-extend”
xxxx xxxx xxxx xxxx xxxx xxxx
x
byte loaded
This bit
zzz zzzz

## Slide 19: C Decisions: if Statements
2 kinds of if statements in C
  if (condition) clause
  if (condition) clause1 else clause2
Rearrange if-else using goto and labels into:
  if (condition) goto L1;
  clause2;
  goto L2;
  L1: clause1;
  L2:
Not as elegant as if-else, but same meaning

## Slide 20: MIPS Decision Instructions
Decision instructions in MIPS
  beq register1, register2, L1
    beq is “branch if equal”
    same meaning as: if (register1==register2) goto L1
  bne register1, register2, L1
    bne is “branch if not equal”
    same meaning as: if (register1!=register2) goto L1
Called conditional branches
  Can be used to implement complex control-flow constructs for high level langauages

## Slide 21: MIPS Goto Instruction
In addition to conditional branches, MIPS has an unconditional branch:
j label
  Called a Jump Instruction: jump (or branch) directly to the given label without needing to satisfy any condition
  Same meaning as: goto label
Technically, it’s the same as:
  beq $0,$0,label
    Condition always satisfied

## Slide 22: Compiling C if into MIPS
C code
  if (i == j) f=g+h; else f=g-h;
  Use mapping:
  f: $s0, g: $s1, h: $s2, i: $s3, j: $s4
Final compiled MIPS code:
beq $s3,$s4,True # branch i==j
sub $s0,$s1,$s2 # f=g-h(false)
j Fin # goto Fin
True: add $s0,$s1,$s2 # f=g+h (true)
Fin:
Note: Compiler automatically creates labels to handle decisions (branches)
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j
Notes: ). Generally not found in HLL code.

## Slide 23: Loops in C/Assembly (1/3)
Simple loop in C; A[] is an array of integers
  do { g = g + A[i];
  i = i + j;
  } while (i != h);
Rewrite this as:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, base of A $s1, $s2, $s3, $s4, $s5

## Slide 24: Loops in C/Assembly (2/3)
Original code:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Final compiled MIPS code:
Loop: sll $t1,$s3,2 #$t1= 4*i add $t1,$t1,$s5 #$t1=addr A lw $t1,0($t1) #$t1=A[i] add $s1,$s1,$t1 #g=g+A[i] add $s3,$s3,$s4 #i=i+j bne $s3,$s2,Loop# goto Loop # if i!=h
Notes: Do goto first
Then I = I + J
Then 1st 4

## Slide 25: Loops in C/Assembly (3/3)
There are three types of loops in C:
  while
  do… while
  for
Each can be rewritten as either of the other two, so the method used in the previous example can be applied to while- and for- loops as well
Key concept: though there are multiple ways of writing a loop in MIPS, the key to decision making is conditional branch
Notes: Switch as HW? Quiz?

## Slide 26: Inequalities in MIPS (1/3)
General programs need to test < and > as well as equalities (== and != in C)
MIPS inequality instruction:
  slt reg1,reg2,reg3
  “Set on Less Than”
  Meaning:
    if (reg2 < reg3) reg1 = 1;
    else reg1 = 0;
  In computereeze, “set” means “set to 1”, “reset” means “set to 0”
reg1 = (reg2 < reg3);

## Slide 27: Inequalities in MIPS (2/3)
How do we use this? Compile by hand: if (g<h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$0,Less # goto Less # if $t0!=0 # (if (g<h)) Less:
  Branch if $t0 != 0  (g < h)
  Register $0 always contains the value 0, so bne and beq often use it for comparison after an slt instruction
A slt  bne pair means if(… < …)goto…

## Slide 28: Immediates in Inequalities
A slt  beq pair means if(… ≥ …)goto…
There is also an immediate version of slt to test against constants: slti
  C loop
if (g >= 1) goto Loop
Loop: . . .
  MIPS loop
  slti $t0,$s0,1 # $t0 = 1 if # $s0<1 (g<1) beq $t0,$0,Loop # goto Loop # if $t0==0 # (if (g>=1)

## Slide 29: Bitwise Operations
Up until now, we’ve done arithmetic (add, sub,addi ), memory access (lw and sw), and branches and jumps
All of these instructions view contents of register as a single quantity (such as a signed or unsigned integer)
New perspective: view register as 32 raw bits rather than as a single 32-bit number
  We may want to access individual bits (or groups of bits) rather than the whole
  Two new classes of instructions: logical & shift operations

## Slide 30: Logical Operators
Logical instruction syntax:
  op dest, src1, src2
  Op: operation name (and, or, nor)
  Dest: register that will receive value
  Src1: first operand (register)
  Src2: second operand (register) or immediate
Accept exactly 2 inputs and produce 1 output
  Benefit: rigid syntax simpler hardware
  Why nor?
    nor $t0, $t1, $t2 # $t0 = not ($t1 or $t2)
Immediate operands
  andi, ori: both expect the third argument to be an immediate
Notes: Nor $t0, $t1, $t2 # $t0 = not ($t1 or $t2), if $t2=0, $t0=not $t1

## Slide 31: Uses for Logical Operators (1/3)
Use AND to create a mask
  Anding a bit with 0 produces a 0 at the output while anding a bit with 1 produces the original bit
Example:
1011 0110 1010 0100 0011 1101 1001 1010
0000 0000 0000 0000 0000 1111 1111 1111
0000 0000 0000 0000 0000 1101 1001 1010
Mask retaining the last 12 bits

## Slide 32: Uses for Logical Operators (2/3)
A bit pattern in conjunction with AND is called a mask that can conceal some bits
  The previous example a mask is used to isolate the rightmost 12 bits of the bit-string by masking out the rest of the string (e.g. setting it to all 0s)
  Concealed bits are set 0s, while the rest bits are left alone
  In particular, if the first bit-string in the above example were in $t0, then the following instruction would mask it:
  andi $t0,$t0,0xFFF

## Slide 33: Uses for Logical Operators (3/3)
Similarly effect of OR operation
  Oring a bit with 1 produces a 1 at the output while oring a bit with 0 produces the original bit
  This can be used to force certain bits to 1s
Example
  $t0 contains 0x12345678, then after this instruction:
  ori $t0, $t0, 0xFFFF
  $t0 contains 0x1234FFFF (e.g. the high-order 16 bits are untouched, while the low-order 16 bits are forced to 1s)

## Slide 34: Shift
  0011 0100 0101 0110 0111 1000 0000 0000
Move (shift) all the bits in a word to the left or right by a number of bits
  Example: shift right by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0000 0000 0001 0010 0011 0100 0101 0110
  Example: shift left by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000

## Slide 35: Logical Shift Instructions
Shift instruction syntax:
  op dest,reg,amt
  Op: operation name
  Dest: register that will receive value
  Reg: register with the value to be shifted
  Amt: shift amount (constant < 32)
MIPS logical shift instructions:
  sll (shift left logical): shifts left and fills emptied bits with 0s
  srl (shift right logical): shifts right and fills emptied bits with 0s
  MIPS also has arithmetic shift instructions that fills with the sign bit

## Slide 36: Stored Program Concept
Instructions are represented as numbers/bits
Programs are stored in memory — to be read or written just like data
Fetch & execute cycle
  Instructions are fetched and put into a special register
  Bits in the register "control" the subsequent actions
  Fetch the “next” instruction and continue
Processor
Memory
memory for data, programs,
compilers, editors, etc.
Notes: Computers built on 2 key principles:
  1) Instructions are represented as numbers.
  2) Therefore, entire programs can be stored in memory to be read or written just like numbers (data).
Simplifies SW/HW of computer systems:
  Memory technology for data also used for programs

## Slide 37: Instruction Representation
Instructions in MIPS are 32-bit long (one word) and divided into “fields”
  Each field tells computer something about an instruction
We could define different fields for each instruction, but MIPS defines only three basic types of instruction formats due to simplicity
  R-format: register format
  I-format: immediate format
  J-format: jump format

## Slide 38: Instruction Formats
I-format: immediate format
  Instructions with immediates
    Excluding shift instructions
  Data transfer instructions (since the offset counts as an immediate)
  Branches (beq and bne)
J-format: jump format
  j and jal (more details later)
R-format: used for all other instructions
It will soon become clear why the instructions have been partitioned in this way

## Slide 39: R-Format Instructions (1/4)
6
5
5
5
6
5
opcode
rs
rt
rd
funct
shamt
Define six fields of the following number of bits each: 6 + 5 + 5 + 5 + 5 + 6 = 32
  Each field has a name
  Each field is viewed as a 5- or 6-bit unsigned integer, not as part of a 32-bit integer
  5-bit fields can represent any number 0-31 (00000 - 11111) while 6-bit fields can represent any number 0-63 (000000-111111)

## Slide 40: R-Format Instructions (2/4)
6
5
5
5
6
5
opcode
rs
rt
rd
funct
shamt
opcode: partially specifies the operation
  Also implies the instruction format: opcode=0 for all R-type instructions
funct: combined with opcode, exactly specifies the instruction
rs (source register): generally register containing the 1st operand
rt (target register): generally register containing the 2nd operand (note that name is misleading)
rd (destination register): generally register which will receive the result of computation

## Slide 41: R-Format Instructions (3/4)
Notes about register fields:
  Each register field is exactly 5 bits, which means that it can specify any unsigned integer in the range 0-31
  Each of these fields specifies one of the 32 registers by number
  The word “generally” was used because there are exceptions that we’ll see later
    E.g. multiplication will generate a result of 64 bit stored in two special registers: nothing important in the rd field

## Slide 42: R-Format Instructions (4/4)
Final field: shamt
  Shift amount: the amount a shift instruction will shift by
  Shifting a 32-bit word by more than 31 is useless, so this field is only 5 bits (so it can represent the numbers 0-31)
  This field is set to 0 in all but the shift instructions

## Slide 43: R-Format Example
MIPS Instruction: add $8,$9,$10
  Encode to decide the value of each field
    opcode = 0, funct = 32 (look up in table in book)
    rd = 8 (destination)
    rs = 9 (first operand), rt = 10 (second operand)
    shamt = 0 (not a shift)
  Decimal number per field representation
  Binary number per field representation
0
9
10
8
32
0
000000
01001
01010
01000
100000
00000

## Slide 44: I-Format Instructions (1/4)
What about instructions with immediates?
  5-bit field only represents numbers up to the value 31: immediates may be much larger
  Ideally, MIPS would have only one instruction format for simplicity: unfortunately, we need to compromise
  Still, try to define new instruction format that is partially consistent with R-format
    The first three fields of both formats are the same size and have the same names
    The rest three fields in R-format are merged to form a single field for the immediate operand
Notes: Same format? Same length?

## Slide 45: I-Format Instructions (2/4)
6
5
5
16
opcode
rs
rt
immediate
Define four fields of the following number of bits each: 6 + 5 + 5 + 16 = 32
  Again, each field has a name
  Design key
    Only one field is inconsistent with R-format
    Most importantly, opcode is still in the same location

## Slide 46: I-Format Instructions (3/4)
opcode: uniquely specifies an instruction
  No funct field
rs: specifies the only register operand (if there is one)
rt: specifies register which will receive result of computation
  This is why it’s called the target register “rt”
6
5
5
16
opcode
rs
rt
immediate
Notes: This also answers question of why R-format has two 6-bit fields to identify instruction instead of a single 12-bit field: in order to be consistent with other formats.

## Slide 47: I-Format Instructions (4/4)
The immediate field
  Used to specify immediates for instructions with a numerical constant operands
  Used to specify address offset in data transfer instructions: lw, sw, etc.
  Used to specify branch address in bne and beq
  Range
    Both positive and negative numbers
    16 bits  can be used to represent immediate up to 216 different values
    What if the number we want to represent is out of the range?

## Slide 48: I-Format Example
MIPS Instruction: addi $21,$22,-50
  Encode for each field
    opcode = 8 (look up in table in book)
    rs = 22 (register containing operand)
    rt = 21 (target register)
    immediate = -50 (by default, this is decimal)
  Decimal number per field representation
  Binary number per field representation
  Hexadecimal representation: 22D5 FFCEhex
  Decimal representation: 584,449,998ten
8
22
21
-50
001000
10110
10101
1111111111001110
Negative number encoding: 2’s complement

## Slide 49: Large Immediates
Range of immediates is limited
  Length of immediate field is 16 bits
  Considered as a signed number (sign bit)
Arithmetic operands or address offset can be larger
  32-bit data / address in MIPS
  We need a way to deal with a 32-bit immediate in any I-format instruction
Solution:
  Handle it in software + new instruction
  Don’t change the current instructions: instead, add a new instruction to help out

## Slide 50: Large Immediates
New instruction:
  lui register, immediate
  Load Upper Immediate
  Takes 16-bit immediate and puts these bits in the upper half (high order half) of the specified register; lower half is set to 0s
  Example:
    Want to write: addi $t0,$t0, 0xABABCDCD
    Need to write a sequence instead:
    lui $at, 0xABAB ori $at, $at, 0xCDCD add $t0,$t0,$at

## Slide 51: Immediates in Conditional Branches
opcode
rs
rt
immediate
Branch instructions bne and beq
  Field rs and rt specify registers to compare
  Field immediate specify branch address
    16 bit is too small since we have 32-bit pointer to memory
Observation
  Branches are used for if-else, while-loop, for-loop: tend to branch to a nearby instruction
  We only need to know the difference between the branch target and the current instruction address, which is much smaller and 16-bit addressing might suffice in most cases
Notes: Half of all conditional branches Spec2000 benchmarks go to locations < 16 instructions away

## Slide 52: PC-Relative Addressing
Solution to branches in a 32-bit instruction: PC-relative addressing
  PC is the special register containing the address of the current instruction
  New program counter = PC + branch address
    Let the 16-bit immediate field be a signed two’s complement integer to be added to the PC if we take the branch
Now we can branch ± 215 bytes from the PC, which should be enough to cover almost any loop
  Any ideas to further optimize this?

## Slide 53: PC-Relative Addressing
Note: Instructions are words, so they are word aligned
  The byte address of an instruction is always a multiple of 4, i.e. it must end with 00 in binary
  The number of bytes to add to the PC will always be a multiple of 4
  Specify the immediate in words
Now, we can branch ± 215 words from the PC (or ± 217 bytes), so we can handle loops 4 times as large

## Slide 54: Branch Address Calculation
Calculation:
  If we do not take the branch:
  PC = PC + 4
    PC+4 = byte address of next instruction
  If we do take the branch:
  PC = (PC + 4) + (immediate * 4)
Observations
  Immediate field specifies the number of words to jump, which is simply the number of instructions to jump
  Immediate field can be positive or negative
  Due to hardware, add immediate to (PC+4), not to PC; will be clearer why later in course

## Slide 55: J-Format Instructions
J-format is used by MIPS jump instructions
  j and jal
  6-bit opcode + 26-bit jump address
Key concepts
  Keep opcode field identical to R-format and I-format for consistency
  Combine all other fields to make room for large target address
    Goto statements and function calls tend to have larger offsets than branches and loops
6 bits
26 bits
opcode
target address

## Slide 56: J-Format Addressing
We have 26 bit to specify the target address
  We cannot fit both a 6-bit opcode and a 32-bit address into a single 32-bit word, so we compromise
  Like branches, jumps will only jump to word aligned addresses  the 26-bit field covers 28 bits of the 32-bit address space
Where do we get the other 4 bits?
  Take the 4 highest order bits from the PC
  Technically, this means that we cannot jump to anywhere in memory, but it’s adequate 99.9999…% of the time, since programs aren’t that long
    Only if straddle a 256 MB boundary
  If we absolutely need to specify a 32-bit address, we can always put it in a register and use the jr instruction
Notes: last two bits are always 00 (in binary): take for granted ; not bother to specify

## Slide 57: J-Format Addressing
Target address calculation
  New PC = { PC[31..28], target address, 00 }
  Understand where each part came from!
  Note: { , , } means concatenation { 4 bits , 26 bits , 2 bits } = 32 bit address
  { 1010, 11111111111111111111111111, 00 } = 10101111111111111111111111111100

## Slide 58: Arithmetic Logic Unit
The ALU is a digital circuit that provides arithmetic and logic operations. It is the fundamental building block of the central processing unit of a computer.
A modern CPU has a very powerful ALU and it is complex in design.

## Slide 59
In addition to ALU modern CPU contains a control unit and a set of registers.
Most of the operations are performed by one or more ALU’s, which load data from the input register. Registers are a small amount of storage available to the CPU.
These registers can be accessed very fast. The control unit tells ALU what operation to perform on the available data.
After calculation/manipulation, the ALU stores the output in an output register.

## Slide 60: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations

## Slide 61: Possible Representations

## Slide 62: MIPS: 32-bit signed integers

## Slide 63: Addition and Subtraction

## Slide 64: Add and Subtract

## Slide 65: Overflow with Unsigned
Overflow with unsigned integers (commonly used for memory addresses) are ignored.
So, recognize overflow and raise exceptions in
  add, addi, sub
Ignore overflow and do not raise exceptions in
  addu, addiu, subu
  addiu $s1, $s1, 35

## Slide 66: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor 0) instruction can retrieve EPC value, to return after corrective action

## Slide 67: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product

## Slide 68: Multiplication Hardware
Initially 0

## Slide 69: Example : 2 x 3

## Slide 70: Optimized Multiplier
Perform steps in parallel: add/shift

## Slide 71: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 72: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 73: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor

## Slide 74: Division

## Slide 75: Division: 7 by 2

## Slide 76: Division Hardware
Initially dividend
Initially divisor in left half

## Slide 77: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 78: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 79: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized

## Slide 80: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 81: Floating Point
Single Precision
In general, the floating point numbers are of the form,
Double Precision

## Slide 82: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1023
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 83: IEEE 754 format
Floating point numbers needs to be compared easily – for sorting
Placing the exponent before significand
Negative exponents pose a challenge to simplified sorting
Biased Notation – bias being subtracted from the normal, unsigned representation
So, the exponent in IEEE 754 format is

## Slide 84: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 85: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 86: Zero, Infinity and NaN

## Slide 87: Denormalized Numbers
Numbers represented in Unnormalized form

## Slide 88: IEEE 754 Encoding Summary

## Slide 89: Floating Point Example

## Slide 90
Example

## Slide 91: Example

## Slide 92: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 93: FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
FP instructions operate only on FP registers
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
    e.g., ldc1 $f8, 32($sp)

## Slide 94: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, lt, le, …)
  Sets or clears FP condition-code bit
    e.g. c.lt.s $f3, $f4
Branch on FP condition code true or false
  bc1t, bc1f
    e.g., bc1t TargetLabel

## Slide 95: FP Instructions in MIPS

## Slide 96: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002p!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  Discovered by Prof. Thomas R. Nicely
  Intel: “The common user would experience it once in 27 years”
  IBM: “Bug occurs once in 24 days”
  Intel apologized and made replacements on request

## Slide 97: Intel Pentium FDIV Bug
  Can be checked using Windows Calculator of MS Excel in Windows 95/98 in a computer with the Pentium line of processors

## Slide 98: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements

## Slide 99: Subword Parallellism
Graphics and audio applications can take advantage of performing simultaneous operations on short vectors
  Example: 128-bit adder:
    Sixteen 8-bit adds
    Eight 16-bit adds
    Four 32-bit adds
Also called data-level parallelism, vector parallelism, or Single Instruction, Multiple Data (SIMD)

## Slide 100: x86 FP Architecture
Originally based on 8087 FP coprocessor
  8 × 80-bit extended-precision registers
  Used as a push-down stack
  Registers indexed from TOS: ST(0), ST(1), …
FP values are 32-bit or 64 in memory
  Converted on load/store of memory operand
  Integer operands can also be converted on load/store
Very difficult to generate and optimize code
  Result: poor FP performance

## Slide 101: Streaming SIMD Extension 2 (SSE2)
Adds 4 × 128-bit registers
  Extended to 8 registers in AMD64/EM64T
Can be used for multiple FP operands
  2 × 64-bit double precision
  4 × 32-bit double precision
  Instructions operate on them simultaneously
    Single-Instruction Multiple-Data

## Slide 102: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow

## Slide 103: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 104: Instruction Fetch
32-bit register
Increment by 4 for next instruction

## Slide 105: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 106: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 107: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 108: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 109: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 110: R-Type/Load/Store Datapath

## Slide 111: Full Datapath

## Slide 112: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 113: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 114: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 115: Datapath With Control

## Slide 116: R-Type Instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6

## Slide 117: Load Instruction
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0

## Slide 118: Branch-on-Equal Instruction
4
rs
rt
address
31:26
25:21
20:16
15:0

## Slide 119: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 120: Datapath With Jumps Added
2
address
31:26
25:0

## Slide 121: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 122: Pipelining

## Slide 123: Pipelining
Process of arrangement of hardware elements of CPU in such way that its overall performance is increased.
Simultaneous execution of more than one process at a time.
Overlapping in execution

## Slide 124: Pipelined vs Non-Pipelined
1 CC for Instruction
5 Stages (K)
8 Instructions (n)
[ K + (n – 1) ] CC
Speedup = NP/P
Efficiency/Utilisation = Blocks used/ Blocks there

## Slide 125: Question – GATE CS 2004
A 4 - stage pipeline has the stage delays as 150, 120, 160 and 140 nanoseconds respectively. Registers that are used between the stages have a delay of 5 nanoseconds each. Assuming constant clocking rate, the total time taken to process 1000 data items on this pipeline will be
Answer: 165.5 ms

## Slide 126: Question – GATE CS 2015
Consider a non-pipelined processor with a clock rate of 2.5 gigahertz and average cycles per instruction of four. The same processor is upgraded to a pipelined processor with five stages; but due to the internal pipeline delay, the clock speed is reduced to 2 gigahertz. Assume that there are no stalls in the pipeline. The speed up achieved in this pipelined processor is __________.
Answer: 3.2

## Slide 127: Hazards in pipelining
Data Hazards
  RAW To
  WAW Output
  WAR Anti
Structural Hazards
Control Hazards

## Slide 128: Question – GATE CS 2018
The instruction pipeline of a RISC processor has the following stages: Instruction Fetch (IF), Instruction Decode (ID), Operand Fetch (OF), Perform Operation (PO) and Writeback (WB), The IF, ID, OF and WB stages take 1 clock cycle each for every instruction. Consider a sequence of 100 instructions. In the PO stage, 40 instructions take 3 clock cycles each, 35 instructions take 2 clock cycles each, and the remaining 25 instructions take 1 clock cycle each. Assume that there are no data hazards and no control hazards.
The number of clock cycles required for completion of execution of the sequence of instruction is ______ .
Answer: 219

## Slide 129: Question – GATE CS 2022
A processor X1 operating at 2 GHz has a standard 5-stage RISC instruction pipeline having a base CPI (cycles per instruction) of one without any pipeline hazards. For a given program P that has 30% branch instructions, control hazards incur 2 cycles stall for every branch. A new version of the processor X2 operating at same clock frequency has an additional branch predictor unit (BPU) that completely eliminates stalls for correctly predicted branches. There is neither any savings nor any additional stalls for wrong predictions. There are no structural hazards and data hazards for X1 and X2. If the BPU has a prediction accuracy of 80%, the speed up (rounded off to two decimal places) obtained by X2 over X1 in executing P is ______.
Answer: 1.428